## Slide 1: Traditional and Alternative Fermentation Techniques
Travis Audet
Anheuser-Busch
October 8, 2015

## Slide 2: The Absolutes of Fermentation
1)

## Slide 3: The Absolutes of Fermentation
1) There are no absolutes in fermentation

## Slide 4: The Absolutes of Fermentation
1) There are no absolutes in fermentation
2) See rule number #1

## Slide 5: The Non-Absolutes of Fermentation
Why no absolutes?
  Difference between ale, lager and other yeasts
  Differences between yeasts in in the same family
    Not all lager behave the same and not all ales etc.
  Absolutes don’t indicate degree of impact
  Other variables are not the same as the one reference
    Estery yeast or low ester yeast?
    Fermenting standard gravity or ferment high gravity?
    Low attenuation or highly attenuated beer?
    Standard fermentation rate or rapid?
    Yeast flocculation characteristics of particular yeast?
    The inherent genetic stability of a strain?
    Fermentation more complex than one parameter causing one result

## Slide 6: Fermentation Good Practices - Temperature
fermentor full temperature should be a degree below fermentation temperature
This prevents cooling coming on before fermentation is vigorous
  Early cooling creates localized temperature gradients before fermentation is robust
  Early cooling can shock yeast
  Early cooling can prolong fermentation

## Slide 7: Fermentation Good Practices – Fill Time
Long fermentor fill times should be avoided
  Track and control hours from yeast/oxygen addition to fermentor fill as a critical control parameter
  Depending on aeration/oxygenation rates and fill frequencies yeast can move in and out of anaerobic condition
  Yeast growth can be excessive
  Stratification of tank can become an issue
If long fill times cannot be avoided then:
  Aerate instead of oxygenation to aid in mixing
  Don’t add yeast on early brews
  Always aerate the final brew

## Slide 8: fermentor Fills
Fill number maximum typical 4 brews single brew lane or 8 brews for double brew lanes
  Single brew lane fills every 2hrs – Total time 4 brews = 8hrs
  Double brew lanes fill every 1hrs – Total time 8 brews = 8hrs

## Slide 9: Fermentation Good Practices
Avoid growing too much yeast
Typical peak cell count is 80 – 100 million cells/ml depending on original gravity
  Greater peak cell counts can lead to loss of beer yield
  Greater peak cell counts can lead to autolysing yeast if not removed mechanically
  Greater peak cell counts can lead to greater peak diacetyl
    Use of FAN beyond valine produces more diacetyl
  Greater peak cell counts can lead to poor yeast health in beers brewed with higher proportions of adjuncts

## Slide 10: Fermentation Good Practices
Avoid high hydrostatic pressures
  Some yeast sensitive to CO2 in solution
  Large tank ratios 2:1 Height to Diameter max
  Greater the pressure then lower the ester formation
Avoid temperature shocking yeast
  Gentle cooling preferably with proportional control valves
  1 degree per hour cooling programs
Final cooling of fermentor should be based on VDK analysis
  Never adjust attenuation level through cooling instead fermentability needs to be controlled through mashing scheme

## Slide 11: Yeast Metabolism and Flavor Active Compounds
FEMS Yeast Research Volume 8, Issue 7, pages 1018-1036, 15 SEP 2008 DOI: 10.1111/j.1567-1364.2008.00433.x http://onlinelibrary.wiley.com/doi/10.1111/j.1567-1364.2008.00433.x/full#f3

## Slide 12: General Fermentation Schemes
Perhaps the first photograph of men drinking beer, circa 1844 in Scotland, by Hill & Adamson

## Slide 13: General Fermentation Schemes – 2 Vessel
Traditional approach is 2 vessel fermentation
Ferment 80 – 90% of extract and then transfer to a second vessel
Advantages:
  re-suspend yeast for finishing beer more quickly
  blending opportunities
  greater throughput for initial vessel
  Maximize tank capacity of second vessel
Disadvantages:
  Additional transfer and losses, additional utilities to support secondary tanks

## Slide 14: General Fermentation Schemes – 2 Vessel with Krausening
Similar to the two vessel system but with fresh wort added
What is krausening?
  Add fresh wort at a rate of 10-20% and typically fresh yeast and air/oxygen when 80% of fermentation is complete
  Fresh wort, yeast and air/oxygen is added at time of transfer of primary fermentor
Why krausen?
  Fresh wort and yeast re-invigorates fermentation to help drive completion of the fermentation and VDK reduction in a shorter amount of time
  Good for yeasts that tend to settle out

## Slide 15: General Fermentation Schemes – 2 Vessel with Krausening
Advantages
  Faster fermentation
Disadvantages
  Added complexity
  The krausen brews need to be planned for addition at the right time
    Possibility of a wort holding tank
  Added risk of microbiological contamination
  Vessel utilization is lower as freeboard is needed in second vessel

## Slide 16: General Fermentation Schemes – Conical fermentor Two Vessel System
A conical fermentor is a vertical fermentor with a cone that allows cone collecting yeast (AKA Cylindro Conical Vessel CCV)
It can be used as a two vessel system
Advantages
  Same as two vessel system already described
  Additionally yeast harvest can be collected from cone avoiding stress of centrifuge collection
  Yeast can be collected earlier in process so presumably healthier
  If used as only primary fermenting vessel does not need to be pressure rated
Disadvantages
  Same as two vessel system already described
  Need flocculent yeast

## Slide 17: General Fermentation Schemes – Conical fermentor Single Vessel System
More recent approach is to use a single vessel for fermentation and maturation (also known as Uni-Tank )
Ferment all extract, reduce VDK’s, settle/collect yeast and age beer all in one tank
  Advantages
    Less tank movements and loses
    Less CIP’s
    Lower contamination risk
    Multiple yeast removals lowering downstream loading
  Disadvantages
    Lower capacity utilization
    Limited to flocculent yeast varieties
    Vessels are more expensive (need pressure rated vessels)
    Lower downstream blending opurtunities

## Slide 18: Lager Fermentation

## Slide 19: Traditional Lager Fermentation
Cool in at 6-7C (43-45F) and free rise to 9C (48F)
  Hold until entire fermentation is complete
  Primary 6-8 days but secondary can be an additional 14 days or longer
Advantages
  Reduced higher alcohol production
  Reduced ester production
  Reduced protease activity so better head retention in final beer
Disadvantages
  Slow

## Slide 20: “Warmer” Lager Fermentations
Cool in at 9C (48F) and free rise to 11C (52F)
  Hold until entire fermentation is complete
  Primary 6-8 days but secondary can be an additional 10 days or longer
Advantages
  Lower higher alcohol production
  Lower ester production
  Lower protease activity so better head retention in final beer
  Slightly faster
Disadvantages

## Slide 21: “Warmer” Lager Fermentations
Cool in at 9C (48F) and free rise to 11C (52F)
  Hold until entire fermentation is complete
  Primary 6-8 days but secondary can be an additional 10 days or longer
Advantages
  Lower higher alcohol production
  Lower ester production
  Lower protease activity so better head retention in final beer
  Slightly faster
Disadvantages
  Still slow

## Slide 22: Rapid Lager Fermentation
Push lager fermentation to fastest possible rate while maintaining sensory profile and yeast health
Esters are formed during yeast growth phase and set at peak cell count
Concept is to allow fermentation to warm after peak cell count
Free rise fermentations allow for rapid reduction of diacetyl to acetoin

## Slide 23: Rapid Lager Fermentation
J. Inst. Brew., September-October, 1990, Vol. 96, pp. 327-331
ESTER FORMATION IN BREWERY FERMENTATIONS
By Hilary A. B. Peddie

## Slide 24: Rapid Lager Fermentation
Starting temperature = ?
  Depends of ester profile, yeast and sensory match to be achieved
Free rise initiation = end of cell growth
Free rise temperature = ?
  Temperature depends on yeast strain and ability to handle fermentation at higher temperatures
Cooling on at end of fermentation
  Typically when VDK is in specification

## Slide 25: Rapid Lager Fermentation
Advantages
  Faster overall fermentation time
  Better vessel utilization
Disadvantages
  Greater foaming and need for lower percentage fills of fermentor or anti-foams to maintain fill levels
  More stressful on yeast but yeast dependent
  Protease enzyme is more active at warmer temperatures and can reduce foam stability in the final beer.

## Slide 26: Ale Fermentation

## Slide 27: Ale Fermentations
Typical ale fermentations 1million cells/ml per degree plato
Oxygen requirement tends to be lower than lagers
~0.75ppm oxygen per degree plato
  i.e standard 12 plato is 9ppm
  i.e. high gravity wort at 17.5 plato 13ppm
Typical ale starts warmer than lager and free rises to a warmer temperature
  Typical starting is 18 - 19C (64 - 66)
  Typical free rise is 20C (68 F)

## Slide 28: Ale Fermentations
Ales tend to be flocculent
Keeping yeast in suspension can be a challenge with some yeasts
  Lower yeast in suspension at the end of fermentation the slower the diacetyl reduction is
Opportunity for a two vessel system to help rouse the yeast
For open vessel fermentations rousing goosenecks can be used to help re-suspend yeast
Some ales are top cropping others are bottom cropping
  Bottom cropping can be collected the same as lager
  Top cropping yeasts need to be collected from the top of the vessel either with scoops or funnel device

## Slide 29: Ale Fermentations

## Slide 30: Yorkshire Squares
Two floored vessel to aid in top cropping yeast

## Slide 31: So Bring on the Alternative!

## Slide 32: Burton Union System

## Slide 33: Continuous Fermentation

## Slide 34: Alternative Aeration Timing
  Testing of VHG 22 Plato worts found it is better to oxygenate 12hrs after pitching wort with yeast rather than at time of filling
  33% reduction in fermentation time with good VDK & ester results
Oxygen levels reached = 25ppm through fermentor oxygenation
  Inline only capable of 9ppm
J. Inst. Brew. 113(2), 168–184, 2007
The Combined Effects of Oxygen Supply Strategy, Inoculum Size and Temperature Profile on Very-High-Gravity Beer Fermentation by Saccharomyces cerevisiae By Heather Jones

## Slide 35: Fermentation Good Practices- Alternative Aeration Timing

## Slide 36: Closing
Thanks to:
  All brewers that contribute and share knowledge of the art and science of brewing
  MBAA
  Anheuser-Busch for their support in presenting today

## Slide 37: Thank You