## Slide 1: Analytical Characterization of Mouthfeel Using a Tribological Method with Test-Brewed Beers
Tomohiro Koizumi
SAPPORO BREWERIES LTD.
1
Notes: Thank you, for kind introduction.
I’m Tomohiro Koizumi from Sapporo breweries in Japan. Today, I will present our recent study, titled ‘Analytical Characterization of Mouthfeel Using a Tribological Method with Test-Brewed Beers’.
SAY:
Good morning everyone and welcome to today’s session. The [name association] presents [name of session title].
I would like to introduce myself. I am [insert name], from [company] and I am [position at company, brief relationship to association or topic] and I will be moderating the session.

## Slide 2
Agenda
Introduction
Materials and Methods
Results
-Beer color and BU
-Filtration
-Ingredients
-Dose tribology change due to staling?
Conclusion
2
Notes: This is today's agenda.
First, I will explain the background of the study.
Next, I will talk about the test methods and test examples.
In the third part, I will present the evaluation results of the samples tested with each parameter.
Lastly, I will summarize the main findings of this study.

## Slide 3
Agenda
Introduction
Materials and Methods
Results
-Beer color and BU
-Filtration
-Ingredients
-Dose tribology change due to staling?
Conclusion
3
Notes: I will now provide an introduction to mouthfeel and tribology.

## Slide 4: What is Mouthfeel?
The mouthfeel plays a significant role in the sensory evaluation of beer.
However, it is still an unknown entity compared to aroma and taste.
Introduction
Notes: The mouthfeel plays a significant role in the sensory evaluation of beer.
Various methods have been developed to analyze mouthfeel.
Although reports are available on mouthfeel, it is still an unknown entity compared to aroma and taste.

## Slide 5: Physical methodology food texturing
Rheology ： Viscosity, Elasticity
Tribology ： Friction, Lubrication
Morphology ： Rough-Smooth, Large-Small
Introduction
Nakamura, 2018
Notes: According to Nakamura, the physical methodology of food texturing can be divided into three categories: rheology, tribology, and morphology.
Of these three categories, rheology is measured in beverages.
However, when describing the mouthfeel of a beer, viscosity alone is often not enough to explain it.

## Slide 6: Physical methodology food texturing
Rheology ： Viscosity, Elasticity
Tribology ： Friction, Lubrication
Morphology ： Rough-Smooth, Large-Small
Introduction
Nakamura, 2018
Notes: Therefore, this study focused on the tribology of alcoholic beverages.
Tribology is the study of friction and lubrication

## Slide 7: What is Tribology?
Rheology focuses on the study of viscosity, whereas tribology focuses on the study of friction.
Tribology is the science and technology related to mutually interacting surfaces in relative motion.
Introduction
Notes: In beverages, rheology focuses on the study of viscosity, whereas tribology focuses on the study of friction.
Tribology is the science and technology related to mutually interacting surfaces in relative motion.
In recent years, there have been reports of tribological measurements for beverages.

## Slide 8: Rheological and Tribological analysis methods
Rheometer
rotates a cylinder system and measures its stress levels.
Tribometer
spins a ball and measures the friction occurring at the interface between the pin and ball.
Introduction
Sample beer
Ball
Pin
Sample beer
Viscosity
Friction
Notes: This slide depicts the rheological and tribological analysis methods.
A rheometer measures viscosity by rotating a cylinder system and measures its stress levels.
Tribology can be measured by changing the attachment of the rheometer.
A tribometer spins a ball and measures the friction occurring at the interface between the pin and ball

## Slide 9: To simulate intraoral friction
A tribometer is used to measure the friction between two surfaces.
Swallowing
Tribology measurements
Ball
Pin
Introduction
9
Sample
Kajita, 2019
Palate
Tongue
Notes: As shown in the previous slide, tribological measurements assess the friction between the pin and ball.
At the start of the measurement, the pin and ball are in contact.
As the ball rotates faster, the sample liquid is drawn into the space between the pin and ball.
When we swallow food items and drinks, they move between the palate and tongue to reach the throat.
The food items or drinks move while in contact with the surface of the oral cavity.
Therefore, it is thought that tribological analysis can simulate intraoral friction.

## Slide 10: Previous study on tribology of beer
Tribological data on both five regular and five non-alcoholic commercial beers.
  Based on the frictional parameters of the beers, clear differences were observed between alcoholic and non-alcoholic beers.
  The beers could be distinguished into those with plain and complex mouthfeel depending on their alcohol content.
In this study we used test beers to measure tribology with different parameters other than alcohol.
Introduction
Fox et al., 2021
Fox et al., 2021
Notes: Fox et al. have performed a tribological analysis of beer, providing tribological data for five regular and five non-alcoholic beers.
Based on the frictional parameters of the beers, clear differences were observed between alcoholic and non-alcoholic beers.
The beers could be distinguished into those with plain versus complex mouthfeels depending on their alcohol contents.
In this study we used test beers to measure tribology with different parameters other than alcohol.

## Slide 11: In this study
We investigated whether tribological analysis can be used to evaluate the mouthfeel of beer.
We evaluated the effects of malt types, BUs, and beer filtration, among others.
  We test brewed with different parameters.
  Tribological measurements, sensory evaluations, and other analyses were also performed.
Introduction
Notes: In this study,
we investigated whether tribological analysis can be used to evaluate the mouthfeel of beer.
we evaluated the effects of malt type, BUs and beer filtration.

## Slide 12
Agenda
Introduction
Materials and Methods
Results
-Beer color and BU
-Filtration
-Ingredients
-Dose tribology change due to staling?
Conclusion
12
Notes: Next, I will talk about the test method and test examples.

## Slide 13: Materials and Methods
Ball-on-3-pins tribology attachment
Rheometer
Measuring conditions
Concentric cylinder system
MCR502 (Anton Paar GmbH)
Tribometer
100L-scale pilot brewing
or commercial samples
Samples
https://www.anton-paar.com/us-en/products/group/rheometer/
Notes: The beer used in this study was brewed in a 100-L-scale pilot plant.
We also used commercial samples.
We used an Anton Paar MCR502 device for the measurements.
For the rheological measurements, we used a concentric cylinder system.
We used a ball-on-a 3-pin tribology attachment for the tribological measurements.

## Slide 14: Measurement example 5 %EtOH, Beer
Chart: 
Chart: 
| 0.01 | 1.5900000000000001E-2 | 2.52E-2 | 3.9899999999999998E-2 | 6.3100000000000003E-2 | 0.1 | 0.159 | 0.251 | 0.39800000000000002 | 0.63100000000000001 | 1 | 1.58 | 2.5099999999999998 | 3.98 | 6.31 | 10 | 15.8 | 25.1 | 39.799999999999997 | 63.1 | 100 | 158 | 251 | 398 | 631 | 1000
5 %EtOH | 59.512 | 101.72 | 132.6 | 84.119 | 42.532 | 20.711 | 10.029 | 4.3397 | 2.137 | 1.6955 | 1.2924 | 1.3714 | 1.3126 | 1.4416 | 1.3375 | 1.3622 | 1.3732 | 1.3506 | 1.389 | 1.416 | 1.4783 | 1.5756 | 2.3988 | 2.9413 | 3.6611 | 4.5816
BeerA(5 %) | 2.9631 | -5.6719 | -6.5649 | -0.88086 | -0.92834 | 2.2674 | 0.98916 | 2.0075 | 1.684 | 1.4774 | 1.7865 | 1.7725 | 1.6642 | 1.5623 | 1.5535 | 1.5798 | 1.6119 | 1.6065 | 1.6267 | 1.6886 | 1.7743 | 1.8228 | 2.482 | 3.2462 | 4.2574 | 5.1054
static friction
stick slip
kinetic friction
Swallowing speed range
Friction Factor μ
Sliding Velocity (m/s)
Viscosity (mPa·s)
Share rate (1/s)
Tribometer
Rheometer
Notes: This slide shows an example of rheometer and tribometer test results.
The left figure shows the test results of the rheometer and the right figure shows the test results of the tribometer.
In this measurement, 5% ethanol and 5% alcohol beer were used.

## Slide 15: Measurement example 5 %EtOH, Beer
Chart: 
Chart: 
| 0.01 | 1.5900000000000001E-2 | 2.52E-2 | 3.9899999999999998E-2 | 6.3100000000000003E-2 | 0.1 | 0.159 | 0.251 | 0.39800000000000002 | 0.63100000000000001 | 1 | 1.58 | 2.5099999999999998 | 3.98 | 6.31 | 10 | 15.8 | 25.1 | 39.799999999999997 | 63.1 | 100 | 158 | 251 | 398 | 631 | 1000
5 %EtOH | 59.512 | 101.72 | 132.6 | 84.119 | 42.532 | 20.711 | 10.029 | 4.3397 | 2.137 | 1.6955 | 1.2924 | 1.3714 | 1.3126 | 1.4416 | 1.3375 | 1.3622 | 1.3732 | 1.3506 | 1.389 | 1.416 | 1.4783 | 1.5756 | 2.3988 | 2.9413 | 3.6611 | 4.5816
BeerA(5 %) | 2.9631 | -5.6719 | -6.5649 | -0.88086 | -0.92834 | 2.2674 | 0.98916 | 2.0075 | 1.684 | 1.4774 | 1.7865 | 1.7725 | 1.6642 | 1.5623 | 1.5535 | 1.5798 | 1.6119 | 1.6065 | 1.6267 | 1.6886 | 1.7743 | 1.8228 | 2.482 | 3.2462 | 4.2574 | 5.1054
static friction
stick slip
kinetic friction
Swallowing speed range
Friction Factor μ
Sliding Velocity (m/s)
Viscosity (mPa·s)
Share rate (1/s)
Tribometer
Rheometer
It is suggested that the viscosity was increased by the extract in the beer.
Notes: A rheometer can measure viscosity.
The swallowing speed of a typical human is thought to be approximately 30–100 (1/s).
In this range, the viscosity of beer was higher than that of ethanol.
It is suggested that the viscosity was increased by the extract in the beer.

## Slide 16: Measurement example 5 %EtOH, Beer
Chart: 
Chart: 
| 0.01 | 1.5900000000000001E-2 | 2.52E-2 | 3.9899999999999998E-2 | 6.3100000000000003E-2 | 0.1 | 0.159 | 0.251 | 0.39800000000000002 | 0.63100000000000001 | 1 | 1.58 | 2.5099999999999998 | 3.98 | 6.31 | 10 | 15.8 | 25.1 | 39.799999999999997 | 63.1 | 100 | 158 | 251 | 398 | 631 | 1000
5 %EtOH | 59.512 | 101.72 | 132.6 | 84.119 | 42.532 | 20.711 | 10.029 | 4.3397 | 2.137 | 1.6955 | 1.2924 | 1.3714 | 1.3126 | 1.4416 | 1.3375 | 1.3622 | 1.3732 | 1.3506 | 1.389 | 1.416 | 1.4783 | 1.5756 | 2.3988 | 2.9413 | 3.6611 | 4.5816
BeerA(5 %) | 2.9631 | -5.6719 | -6.5649 | -0.88086 | -0.92834 | 2.2674 | 0.98916 | 2.0075 | 1.684 | 1.4774 | 1.7865 | 1.7725 | 1.6642 | 1.5623 | 1.5535 | 1.5798 | 1.6119 | 1.6065 | 1.6267 | 1.6886 | 1.7743 | 1.8228 | 2.482 | 3.2462 | 4.2574 | 5.1054
static friction
stick slip
kinetic friction
Swallowing speed range
Friction Factor μ
Sliding Velocity (m/s)
Viscosity (mPa·s)
Share rate (1/s)
Tribometer
Rheometer
Static and kinetic friction were reduced by various beer components.
The stick-slip phenomenon was stronger in ethanol solution than in beer.
Notes: On the other hand, a tribometer measures friction.
The friction factor increased as the sliding velocity increased, and it decreased when it exceeded the static friction force.
The stick–slip phenomenon occurred on the right side, where the peak moved upward and downward.
Static and kinetic friction were reduced by various beer components.
The stick–slip phenomenon was stronger in ethanol solution than in beer.
We performed these two analyses on various beers.

## Slide 17: Test conditions
Parameter | 
Alcohol content | 5, 7, 9 %
BU | 16, 51 unit
Color | 6, 125 °EBC
Malt type | Barley, Wheat
Filtration | 
Ingredients | Lactose, Whey
Staling | 
Notes: This is the list of the test conditions for the test beers used in this study.

## Slide 18
Agenda
Introduction
Materials and Methods
Results
-Beer color and BU
-Filtration
-Ingredients
-Dose tribology change due to staling?
Conclusion
18
Notes: In the next section, I will explain the results of our analysis.

## Slide 19: Result：Can detect differences?
Parameter |  | Rheology | Tribology
Alcohol content | 5, 7, 9 % | Yes | Yes
BU | 16, 51 unit | No | No
Color | 6, 125 °EBC | No | Yes
Malt type | Barley, Wheat | No | Yes
Filtration |  | No | Yes
Ingredients | Lactose, Whey | No | Yes
Staling |  | No | Yes
Trial 1
Trial 2
Trial 3
Trial 4
Notes: First, I will present a summary of the results.
We performed rheological and tribological analyses.
The only rheological differences were observed in the samples with different alcohol contents.
On the other hand, most samples exhibited differences in the tribological analysis.
In this presentation, I report the results of these four trials in detail.

## Slide 20: Result：Can detect differences?
Parameter |  | Rheology | Tribology
Alcohol content | 5, 7, 9 % | Yes | Yes
BU | 16, 51 unit | No | No
Color | 6, 125 °EBC | No | Yes
Malt type | Barley, Wheat | No | Yes
Filtration |  | No | Yes
Ingredients | Lactose, Whey | No | Yes
Staling |  | No | Yes
Trial 1
Trial 2
Trial 3
Trial 4
Notes: In Trial 1, we assessed the differences in BU and color.

## Slide 21
Trial 1 BU ,Color
Color (°EBC) 7 120
OG (%) 12.5 12.4
Alc. (%) 5.4 5.5
BU (unit) 16 51
OG (%) 13.7 13.6
Alc. (%) 6.2 6.3
We measured by both the rheological and tribological properties.
Different BUs
(Pilsner type beer)
Different Colors
(Pilsner type beer
or black beer)
Notes: This slide presents the analytical values for the beers used in Trial 1.
We used pilsner-type beers with bitterness units of 16 and 51,
and we also used beers with color intensities of 7 and 120 EBC.
For these samples, we measured by both the rheological and tribological properties.

## Slide 22
Chart: 
Sliding Velocity (m/s)
Friction Factor μ
Tribometer
Rheometer
BU
Color
Trial 1
No difference in viscosity was found. The use of a colored malt resulted in a difference in friction.
Chart: 
| 0.01 | 1.5900000000000001E-2 | 2.5100000000000001E-2 | 3.9800000000000002E-2 | 6.3100000000000003E-2 | 0.1 | 0.158 | 0.251 | 0.39800000000000002 | 0.63100000000000001 | 1 | 1.58 | 2.5099999999999998 | 3.98 | 6.31 | 10 | 15.8 | 25.1 | 39.799999999999997 | 63.1 | 100 | 158 | 251 | 398 | 631 | 1000
7 °EBC | -16.509 | -10.871 | 1.0496 | 0.82958 | 4.1838 | 3.2883 | 1.3003 | 0.64921 | 2.1744 | 1.7106 | 1.7498 | 1.7128 | 1.6886 | 1.7752 | 1.8373 | 1.7708 | 1.7574 | 1.82 | 1.8514 | 1.881 | 1.9209 | 2.0118 | 2.7335 | 3.525 | 4.5587 | 5.3871
120 °EBC | 5.3222 | 5.1489 | 6.5087 | -0.11523 | 4.6376 | 2.0377 | 4.8884 | 1.7601 | 2.7596 | 2.1848 | 2.2252 | 2.0534 | 1.7914 | 1.7093 | 1.7978 | 1.7617 | 1.7934 | 1.8207 | 1.8302 | 1.8961 | 1.9771 | 2.0231 | 2.635 | 3.4559 | 4.5468 | 5.4255
Share rate (1/s)
Viscosity (mPa·s)
Chart: 
| 0.01 | 1.5800000000000002E-2 | 2.5100000000000001E-2 | 3.9800000000000002E-2 | 6.3100000000000003E-2 | 0.1 | 0.158 | 0.251 | 0.39800000000000002 | 0.63100000000000001 | 1 | 1.59 | 2.5099999999999998 | 3.98 | 6.31 | 10 | 15.8 | 25.1 | 39.799999999999997 | 63.1 | 100 | 158 | 251 | 398 | 631 | 1000
BU51 | -28.467 | -21.976 | -10.941 | -7.6576 | -2.3091 | -1.1432 | 1.9338 | -0.43176 | 0.10865 | 1.1944 | 1.3616 | 1.5424 | 1.7518 | 1.7395 | 1.6056 | 1.732 | 1.7247 | 1.6977 | 1.7455 | 1.7793 | 1.853 | 1.9406 | 2.575 | 3.3393 | 4.2957 | 5.2428
BU16 | -16.509 | -10.871 | 1.0496 | 0.82958 | 4.1838 | 3.2883 | 1.3003 | 0.64921 | 2.1744 | 1.7106 | 1.7498 | 1.7128 | 1.6886 | 1.7752 | 1.8373 | 1.7708 | 1.7574 | 1.82 | 1.8514 | 1.881 | 1.9209 | 2.0118 | 2.7335 | 3.525 | 4.5587 | 5.3871
Share rate (1/s)
Viscosity (mPa·s)
Chart: 
Sliding Velocity (m/s)
Friction Factor μ
Notes: TPP 187.78（51）、168.92（16）
This slide shows the results of Trial 1.
First, the rheometer results did not reveal differences in BU or color.
Second, the tribometer results revealed no differences in the BU values but did reveal differences in the colors of the beers.
We found that beers with darker colors exhibited reduced friction.

## Slide 23: Result：Can detect differences?
Parameter |  | Rheology | Tribology
Alcohol content | 5, 7, 9 % | Yes | Yes
BU | 16, 51 unit | No | No
Color | 6, 125 °EBC | No | Yes
Malt type | Barley, Wheat | No | Yes
Filtration |  | No | Yes
Ingredients | Lactose, Whey | No | Yes
Staling |  | No | Yes
Trial 1
Trial 2
Trial 3
Trial 4
Notes: In Trial 2, we applied our analysis to filtered versus unfiltered beers.

## Slide 24: Trial 2 Filtration
I 100% wheat malt Filtered
II 100% wheat malt Unfiltered
OG (%) 12.1 12.0
Alc. (%) 5.1 5.1
I
II
Notes: This slide shows the beer conditions used in Trial 2.
The samples were brewed with 100% wheat malt, and the conditions were changed only for filtration.

## Slide 25: Trial 2 Result : Rheometer and Tribometer
Chart: 
Friction Factor μ
Sliding Velocity (m/s)
static friction
stick slip
kinetic friction
25
Chart: 
| 0.01 | 1.5800000000000002E-2 | 2.5100000000000001E-2 | 3.9800000000000002E-2 | 6.3100000000000003E-2 | 0.1 | 0.158 | 0.251 | 0.39800000000000002 | 0.63 | 1 | 1.58 | 2.5099999999999998 | 3.98 | 6.31 | 10 | 15.8 | 25.1 | 39.799999999999997 | 63.1 | 100 | 158 | 251 | 398 | 631 | 1000
Filtered | -3.9324 | -0.69199 | 3.19 | -0.10371 | 3.8673 | -0.59266 | 0.90505 | 0.57763 | 1.3397 | 1.2737 | 1.5149 | 1.7149 | 1.8033 | 1.8982 | 1.7127 | 1.831 | 1.8216 | 1.7991 | 1.8501 | 1.8784 | 1.9451 | 2.0351 | 2.6871 | 3.4869 | 4.4092 | 5.5644
Unfiltered | -30.324 | -20.698 | -17.353 | -6.7368 | -3.0919 | -1.4259 | 0.38377 | 0.29846 | 1.7959 | 1.4245 | 1.6702 | 1.7936 | 1.8336 | 1.8536 | 1.7237 | 1.8211 | 1.8252 | 1.791 | 1.8368 | 1.8748 | 1.9539 | 2.0317 | 2.6742 | 3.3422 | 4.4738 | 5.4488
Viscosity (mPa·s)
Share rate (1/s)
Static and kinetic friction were reduced in unfiltered beer compared to filtered beer.
Notes: This slide shows the results of the rheological and tribological measurements.
We found no difference in viscosity between filtered and unfiltered samples.
However, we found differences in the tribological analysis.
Static and kinetic friction were reduced in unfiltered beer compared to those in filtered beer.
We then also performed a sensory test.

## Slide 26: Trial 2 Sensory evaluation
Sensory evaluation
Can panelists determine smoothness?
Smoothness
Not
Smoothness
The results of tribological analysis correlated with those of sensory evaluation when comparing unfiltered to filtered beer.
Smoothness
Not
Smoothness
Chart: Smoothness
| Filtered | Unfiltered
 | 2.6667 | 3.6667
*
N=9, p<0.05
Blind-folded and
nose plugged.
Notes: Sensory evaluation was performed using a five-point scale by a panel of nine individuals, with the score increasing as the smoothness increased.
To eliminate appearance and olfactory influences, the test was performed with blind-folded and nose plugs.
The sensory evaluation revealed that the unfiltered beer was considered to be smoother.
The tribological analysis showed that the unfiltered beer had lower friction.
Therefore, the results of the tribological analysis correlated with those of the sensory evaluation when comparing unfiltered to filtered beer.

## Slide 27: Result：Can detect differences?
Parameter |  | Rheology | Tribology
Alcohol content | 5, 7, 9 % | Yes | Yes
BU | 16, 51 unit | No | No
Color | 6, 125 °EBC | No | Yes
Malt type | Barley, Wheat | No | Yes
Filtration |  | No | Yes
Ingredients | Lactose, Whey | No | Yes
Staling |  | No | Yes
Trial 1
Trial 2
Trial 3
Trial 4
Notes: In Trial 3, we applied our analysis to beers with different ingredients.

## Slide 28
Trial3
Trial 3 Ingredients, Lactose or Whey
Lactose or Whey
Notes: Sample beers were brewed by adding lactose or whey at wort boiling.
Whey is a byproduct of cheese production. Whey contains lactose, and some brewers use whey in the brewing of milk stouts.
The test beers had similar amounts of lactose.
On the other hand, protein content was higher in beers made with whey.

## Slide 29
Chart: 
Friction Factor μ
Sliding Velocity (m/s)
stick slip
29
static friction
kinetic friction
Viscosity (mPa·s)
Share rate (1/s)
The addition of lactose increased static and kinetic friction.
On the other hand, the addition of whey, which contained the same amount of lactose, decreased static and kinetic friction.
Chart: 
| 9.9699999999999997E-3 | 1.5800000000000002E-2 | 2.5100000000000001E-2 | 3.9800000000000002E-2 | 6.3100000000000003E-2 | 0.1 | 0.158 | 0.251 | 0.39800000000000002 | 0.63100000000000001 | 1 | 1.58 | 2.5099999999999998 | 3.98 | 6.31 | 10 | 15.8 | 25.1 | 39.799999999999997 | 63.1 | 100 | 158 | 251 | 398 | 631 | 1000
Cont. | 5.3222 | 5.1489 | 6.5087 | -0.11523 | 4.6376 | 2.0377 | 4.8884 | 1.7601 | 2.7596 | 2.1848 | 2.2252 | 2.0534 | 1.7914 | 1.7093 | 1.7978 | 1.7617 | 1.7934 | 1.8207 | 1.8302 | 1.8961 | 1.9771 | 2.0231 | 2.635 | 3.4559 | 4.5468 | 5.4255
Lactose | 21.575 | 25.168 | 17.458 | 8.4404 | 6.2675 | 6.1093 | 4.5139 | 5.2124 | 3.1167 | 3.1663 | 2.4075 | 1.965 | 1.8318 | 1.8377 | 1.9543 | 1.8149 | 1.8343 | 1.8832 | 1.8926 | 1.9297 | 1.9771 | 2.0351 | 2.6485 | 3.4488 | 4.4514 | 5.4454
Whey | 0.17474 | 7.0185 | 4.7651 | 4.5194 | -0.70509 | -0.89203 | -0.027949 | 1.4008 | 1.4655 | 1.9026 | 1.8241 | 1.9446 | 1.8949 | 1.7243 | 1.7336 | 1.7678 | 1.8025 | 1.7845 | 1.8053 | 1.868 | 1.9562 | 2.0091 | 2.6357 | 3.4903 | 4.4639 | 5.3953
Trial 3 Result : Rheometer and Tribometer
Notes: This slide shows the results of the rheometer and tribometer measurements.
The addition of lactose increased static and kinetic friction.
On the other hand, the addition of whey, which contained the same amount of lactose, decreased static and kinetic friction.
Therefore, it is suggested that components other than lactose in whey reduce friction.

## Slide 30
Sensory evaluation
Can panelists determine smoothness?
Chart: 
| Black beer | Lactose | Whey
Smoothness | 3.1 | 3.1 | 4.3
Smoothness
Not
Smoothness
**
*
Smoothness
Not
Smoothness
Nose plugged.
N=10
*p<0.05
**p<0.01
The results of tribological analysis correlated with those of sensory evaluation when comparing beer with lactose and with whey.
Trial3 Sensory evaluation
Notes: Sensory evaluation was performed same method.
To eliminate olfactory influences, this test was performed with nose plugs.
The sensory evaluation revealed that the beer with whey was considered to be smoother.
The tribological analysis showed that the beer with whey had lower friction.
Therefore, the results of the tribological analysis correlated with those of the sensory evaluation when comparing these beers.

## Slide 31: Result：Can detect differences?
Parameter |  | Rheology | Tribology
Alcohol content | 5, 7, 9 % | Yes | Yes
BU | 16, 51 unit | No | No
Color | 6, 125 °EBC | No | Yes
Malt type | Barley, Wheat | No | Yes
Filtration |  | No | Yes
Ingredients | Lactose, Whey | No | Yes
Staling |  | No | Yes
Trial 1
Trial 2
Trial 3
Trial 4
Notes: Finally, in Trial 4, we used storage samples.

## Slide 32: Trial 4 Dose tribology change due to staling?
Pilsner-type beer（commercial）
Storage
for 3 months
at 5, 20, 40 °C
Pilsner-type beer
Rheology
Tribology
Sensory evaluation test
Particle Measurement
Notes: In this trial, we used commercial beer.
The sample beer was stored at 5 °C, 20 °C, or 40 °C for 3 months.
The beer was then tested using a rheometer, a tribometer, sensory evaluation, and particle measurements.

## Slide 33: Trial 4 Result : Rheometer and Tribometer
Chart: 
Friction Factor μ
Sliding Velocity (m/s)
stick slip
33
static friction
kinetic friction
Chart: 
| 9.9600000000000001E-3 | 1.5800000000000002E-2 | 2.5100000000000001E-2 | 3.9800000000000002E-2 | 6.3100000000000003E-2 | 0.1 | 0.159 | 0.251 | 0.39800000000000002 | 0.63100000000000001 | 1 | 1.59 | 2.5099999999999998 | 3.98 | 6.31 | 10 | 15.8 | 25.1 | 39.799999999999997 | 63.1 | 100 | 158 | 251 | 398 | 631 | 1000
5 °C | -15.592 | -4.7741 | -1.7467 | 2.0903 | 1.4062 | 1.4626 | 0.27465 | 1.1689 | 2.1542 | 1.7113 | 1.7484 | 1.7331 | 1.6909 | 1.611 | 1.6919 | 1.6313 | 1.636 | 1.6995 | 1.73 | 1.7617 | 1.8 | 1.8905 | 2.5355 | 3.3783 | 4.2271 | 5.1649
20 °C | 25.809 | 18.508 | 12.615 | 8.5476 | 7.2159 | 5.385 | 4.0403 | 3.3956 | 2.5652 | 2.7375 | 2.2599 | 1.9225 | 1.7313 | 1.7077 | 1.8535 | 1.7232 | 1.7211 | 1.7169 | 1.7381 | 1.7533 | 1.7803 | 1.8704 | 2.5386 | 3.3156 | 4.2348 | 5.1371
40 °C | 10.305 | 5.348 | 8.0392 | 4.4078 | 1.8561 | 1.3577 | 2.608 | 2.9076 | 0.90479 | 1.5263 | 1.4553 | 1.4409 | 1.4853 | 1.6208 | 1.6015 | 1.6245 | 1.6291 | 1.6206 | 1.6681 | 1.6956 | 1.7623 | 1.8508 | 2.5129 | 3.3127 | 4.1512 | 5.1006
Viscosity (mPa·s)
Share rate (1/s)
As the storage temperature increased, both the static and kinetic friction decreased.
Notes: This slide shows the results of the rheometer and tribometer measurements.
We found that as the storage temperature increased, both the static and kinetic friction decreased.

## Slide 34: Trial 4 Sensory evaluation
Chart: velvetiness
| 5 °C | 20 °C | 40 °C
Smoothness | 2.1 | 3.3 | 4.1
Sensory evaluation test
Can panelists determine velvetiness?
Velvetiness
Not
velvetiness
Tribology analysis results and sensory evaluation results were correlated for the stored beer.
***
*
**
N=10
*p<0.05
**p<0.01
***p<0.001
Nose plugged
Notes: Sensory evaluation was performed using a five-point scale by a panel of 10 participants, with the score increasing as the velvetiness increased.
To eliminate olfactory influences, this test was performed with nose plugs.
The sensory evaluation revealed that storage at high temperatures increased the velvetiness.
The tribological analysis showed that beer stored at higher temperatures had lower friction.
Therefore, the tribological analysis and sensory evaluation results were correlated for the stored beer.

## Slide 35
The particle size increased during storage.
Particle diameter (nm)
Relative frequency (%)
Chart: 
Trial 4 Particle Measurement
Litesizer 500, Anton Paar
https://www.anton-paar.com/jp-jp/products/details/litesizer/
Notes: This slide shows the results of the analysis of beer stored using an Anton Paar particle analyzer.
It is well known that particle size increases with increasing storage temperature.
It has been suggested that the increase in particle size results in a change in the mouthfeel in the oral cavity.

## Slide 36: Summary：Can detect differences?
Parameter |  | Rheology | Tribology | Sensory evaluation “mouthfeel”
Alcohol content | 5, 7, 9 % | Yes | Yes | Not tested
BU | 16, 51 unit | No | No | Not tested
Color | 6, 125 °EBC | No | Yes | Not tested
Malt type | Barley, Wheat | No | Yes | Not tested
Filtration |  | No | Yes | Yes
Ingredients | Lactose, Whey | No | Yes | Yes
Staling |  | No | Yes | Yes
Notes: Here is a brief summary of this section.
Beers with similar alcohol contents and extract did not exhibit significantly different rheological properties.
Beers that did not exhibit differences in the rheological analysis nonetheless exhibited differences in the tribological analysis. For example, there were differences in color, filtration, and storage.
Sample beers that exhibited different tribological values also differed significantly in terms of their sensory properties.

## Slide 37
Agenda
Introduction
Materials and Methods
Results
-Beer color and BU
-Filtration
-Ingredients
-Dose tribology change due to staling?
Conclusion
37
Notes: Finally, I would like to summarize the results of this study.

## Slide 38: Conclusion
We measured friction using a tribometer as a parameter related to mouthfeel.
We found differences in tribology between the following samples.
  -Filtration, colored malt, lactose or whey
Differences in friction with storage were observed. These samples exhibited similar differences in sensory characteristics. This suggests a correlation between the tribological analysis results and sensory properties. This may be due to differences in particle size.
Based on these results, we consider that mouthfeel is related to the particles in beer.
Notes: In this study, we reached the following important conclusions:
In many cases, there is a difference in sensory evaluation of mouthfeel, but the difference cannot be detected in viscosity.
We measured friction as a parameter related to mouthfeel using a tribometer.
We found differences between unfiltered and filtered beers, with lactose and with whey, with and without colored malt.
Differences in friction with different storage times were also observed. The samples exhibited differences sensory characteristics. This suggests a correlation between the tribological analysis results and the sensory properties. This may be because of the differences in particle size.
Based on these results, we consider that mouthfeel is related to the particles in beer.

## Slide 39: Future Work
Investigation of factors related to mouthfeel
  What other particles are involved in the mouthfeel?
  Interaction between beer ingredients and the oral cavity
Determine what kinds of particles can improve the mouthfeel
  In this study, we report the relationship between the particles and tribological analysis.
  Not all particles provide a good mouthfeel.
Notes: We plan to further investigate the factors related to mouthfeel and determine what kinds of particles can improve the mouthfeel.

## Slide 40: Resources
Nakamura, T. A Design Method for Creating Novel Food Textures (in Japanese). Food processing and ingredients. 2018, 53(4): 5-7.
Kajita, Y. Food Safety and Tribology: Evaluation of Beverage Texture by Viscoelasticity Measuring (in Japanese). Journal of Economic Maintenance Tribology. 2019; 651:10-14
Fox, D. et al., Mouthfeel of Beer: Development of Tribology Method and Correlation with Sensory Data from an Online Database. Journal of the American Society of Brewing Chemists. 2021
https://www.anton-paar.com/us-en/products/group/rheometer/
https://www.anton-paar.com/jp-jp/products/details/litesizer/
Notes: In addition, the publications referred in this presentation are previous studies.

## Slide 41: Collaborators
Kiyoshi Takoi
Atsushi Tanigawa
Toshihiro Kiyosaki
Notes: I would also like to acknowledge and introduce my colleagues.

## Slide 42: Thank you for your attention
Notes: This is the end of my presentation.
Thank you for your kind attention.

## Slide 43
A
Q
REQUIRED
Notes: SAY:
It’s time to answer some of the questions you’ve been asking from the Q&A panel.
DO:
Make sure to use their name and show appreciation for the comment.

## Slide 44: appendix

## Slide 45
I 100% barley malt
II 100% wheat malt
OG(%) 12.1 12.1
Alc.(%) 5.5 5.1
I
II
Malt type

## Slide 46: Malt type
Chart: 
Friction Factor μ
Sliding Velocity (m/s)
stick slip
46
static friction
kinetic friction
Viscosity (mPa·s)
Share rate (1/s)
Comparison of barley and wheat malt static friction was approximately the same, but the kinetic friction was higher for wheat malt.
Chart: 
| 9.9900000000000006E-3 | 1.5800000000000002E-2 | 2.5100000000000001E-2 | 3.9800000000000002E-2 | 6.3100000000000003E-2 | 0.1 | 0.158 | 0.251 | 0.39800000000000002 | 0.63100000000000001 | 1 | 1.58 | 2.5099999999999998 | 3.98 | 6.31 | 10 | 15.8 | 25.1 | 39.799999999999997 | 63.1 | 100 | 158 | 251 | 398 | 631 | 1000
Barley | 10.247 | 9.4445 | 12.2 | 4.4468 | 8.3523 | 5.3341 | 3.8757 | 2.5484 | 2.5604 | 2.16 | 1.9686 | 2.0411 | 1.6456 | 1.6267 | 1.7497 | 1.691 | 1.7158 | 1.759 | 1.7698 | 1.8334 | 1.9091 | 1.9571 | 2.5571 | 3.4156 | 4.3518 | 5.2944
Wheat | -3.9324 | -0.69199 | 3.19 | -0.10371 | 3.8673 | -0.59266 | 0.90505 | 0.57763 | 1.3397 | 1.2737 | 1.5149 | 1.7149 | 1.8033 | 1.8982 | 1.7127 | 1.831 | 1.8216 | 1.7991 | 1.8501 | 1.8784 | 1.9451 | 2.0351 | 2.6871 | 3.4869 | 4.4092 | 5.5644