## Slide 1: Is PCR enough? A Comprehensive Approach to Quality Control in the Brewery Nicole Balistreri, Quality Manager, Inland Island Laboratories John Giarratano, Owner | Founder, Inland Island Laboratories
Notes: SAY:
Good morning everyone and welcome to today’s session. The [name association] presents [name of session title].
I would like to introduce myself. I am [insert name], from [company] and I am [position at company, brief relationship to association or topic] and I will be moderating the session.

## Slide 2: Discussion
Quality Control is an often overlooked, but powerful tool for breweries of all sizes. It is a protection for owners, stakeholders, and employees to maintain control by monitoring their product from start to finish. However, there is not a one-size-fits-all QC approach for every brewery.
Tailored protocols can be as extensive or narrow as a brewery’s focus requires. The topic of QC can often feel unapproachable and overwhelming given the diversity in available testing methods. Not to mention, the time and expense of diverting resources towards QC can feel unnecessary…until the worst happens. As a solution, many brewers have turned to PCR in the last several years for quick answers, and relatively easy use.
PCR is no doubt a powerful and accurate instrument when used correctly. However, it is only as useful as the questions you ask it. Today’s discussion is an appeal for the use of plating as a guide towards asking the right questions with PCR.
We’ll begin by laying out a short background on different types of PCR, and which type we believe makes the most sense for this application. Then, we’ll briefly discuss some of the pros and cons of traditional plating. Finally, we’ll talk about how to guild the two methods using each other, for a comprehensive and cost saving approach to QC.

## Slide 3: PCR
A brief overview

## Slide 4: Endpoint PCR
End point florescence
Can be prone to false positives, little interpretive recourse
Economical, easy to use

## Slide 5: PCR Kits
Speciated microbial testing
Low upfront cost, can be more expensive per run
Primers pre-set
Microbial load not indicated

## Slide 6: What is qPCR

## Slide 7: Quantitative PCR
Florescence in real time
Presence and concentration of DNA

## Slide 8: Multiplex qPCR
Decision tree-based approach
ID and quantity
Flexibility and choice of primers, useful in cutting back resources
Recommended for simple colony testing. Broader the better

## Slide 9: Traditional Plating
A quick comparison

## Slide 10: Benefits of Traditional Plating
Broad organism testing
Catch everything!
Viability
See reproducibility and deficiency
Plating with use of indicators helps differentiate species
Morphology differences
Cost savings vs. PCR
Low upfront and long-term cost

## Slide 11: Benefits of Traditional Plating
Plating can be tailored
Each step can be targeted
Fewer proprietary components
Plating equipment is everywhere
Non-brewery spoiling organismal growth is an indicator of general hygiene and gaps in cleaning
Examples include bacillus subtilis and bacillus movajensis. Not included in many brewery spoiling qPCR primer sets

## Slide 12: So why doesn’t everyone plate? Drawbacks
  Long incubation times
    4-5 day typical aerobic spoilers, up to 14 days for anerobic
  Finished beer filtration
  Plate making
    Long list of necessary materials
  Potentially hazardous components
    Processes need to be created and executed thoughtfully
  Logistics of buying premade
    Cost, shipping, expiration

## Slide 13: Combination Methods and their application
Plating for broad detection, PCR for ID
Enrichment!
Clarification-
One method validates another
Decrease the cost of PCR by asking the right questions

## Slide 14: Case Studies
Combination method examples

## Slide 15: Morphology Differences

## Slide 16: Fog Machine Yeast vs. Belgian Monk Ale IV

## Slide 17: How to use plate results to dig deeper
Colony testing using PCR
Select for needed primers only!
Microscope analysis
Side by side streaking
Use that Colony!

## Slide 18: Leuconostoc Citreum
-Lactic Acid producing bacteria used commercially in the production of kimchi
-Thermophile
-Caught on cycloheximide enriched plates
-Hop resistance
-ABV resistant up to 7.44%

## Slide 19: Summary
Both methods have individual advantages and drawbacks but are more economical and comprehensive when used in tandem. Plating is best for questions related to broad screening, and qPCR is good for targeting specific answers and organism typing.
Multiplex qPCR is a good option when used in combination with plating due to the flexibility around choosing and excluding primers.
By combining methods, you can achieve significantly more thorough screening, and save money doing it. Win win

## Slide 20: Resources
  Aras J. Klimas (2023). Midwest Microbio Beer qPCR guide [Internal user manual]. Company Archives, Midwest Microbio. Accession Number 008.3.
  Technical Committe, ASBC. “General Culture Media.” ASBC Methods of Analysis, 2011, https://doi.org/10.1094/asbcmoa-microbiologicalcontrol-4.
  Technical Committe, ASBC. “Differential Culture Media.” ASBC Methods of Analysis, vol. 5, 2020, https://doi.org/10.1094/asbcmoa-microbiologicalcontrol-5.
  MillerCoors, and Anheuser-Busch. “Common Brewery-Related Microorganisms.” ASBC Methods of Analysis, www.asbcnet.org/Methods. Accessed 21 Sept. 2023.
REQUIRED
Notes: SAY:
If you found today’s topic particularly interesting, find ways to continue the learning. We’ve provided a few additional resources to extend the topic outside of this session. Write them down. Use your phone to take a picture of this screen. Review the slide deck that came in your session email today. Our association is here to support your goals.
DO:
Locate and additional resources to share with members that extend beyond this session – pubs, websites, name people and share email address or other.

## Slide 21
A
Q
REQUIRED
Notes: SAY:
It’s time to answer some of the questions you’ve been asking from the Q&A panel.
DO:
Make sure to use their name and show appreciation for the comment.